## Slide 1
CHAPTER FOUR
PICTORIAL DRAWING

## Slide 2
1. Objectives
Be able to explain the difference between
Multi-view drawing and pictorial drawing
Be able to create an isometric and oblique sketches from multi-view drawing.
Be able to explain the difference between an axonometric projection and an oblique projection.

## Slide 3
2. Revision

## Slide 4
In multi-view representation of an object, two or more views are used to describe its form or shape and size accurately. However , since each of the views shows only one face and two principal dimensions of an object.

## Slide 5
Pictorial drawing representation of an object showing the three faces on a single plane to represent an object in its realistic appearance.
Or Pictorial drawing is a drawing by which shape and size of an object is expressed in three dimensions to show the three faces (i.e. height, width and depth).

## Slide 7
In spite of its advantage, pictorial drawing has the following limitations as compared to a multi-view drawing:
  it frequently has a distorted and unreal appearance of object being represented,
  relatively required more time to prepare pictorial representation of an object
  it is difficult to measure and to give dimensions.

## Slide 8
3. Types of pictorial drawing
Pictorial drawing is divided into three classifications:
i. Axonometric projection,
ii. Oblique projection, and
iii. Perspective or central projection.

## Slide 9
The difference among the three projection
types is illustrated pictorially as shown

## Slide 10
3.1. Axonometric Projection
A
B
C
D
Parallel each other & normal
to picture plane
Line
of
sight
A
B
C
D

## Slide 11
Axonometric Projection
Type of axonometric drawing
a
b
c
2. Dimetric
Two angles are equal.
b
a
c
3. Trimetric
None of angles are equal.
a
b
c
1. Isometric
All angles are equal.
A
B
C
D
A
B
C
D
Axonometric axis
Axonometric axis
Axonometric axis

## Slide 12
Isometric Projection
& Isometric drawing

## Slide 13
Rotate 45
about vertical axis
Tilt forward (35o16’)
3.1.1.Isometric Projection
All edges foreshorten
about 0.8 time.

## Slide 14
Isometric Drawing
Isometric drawing is a drawing drawn on an isometric axes using full scale.
Isometric projection
(True projection)
Isometric drawing
(Full scale)
Forshorten
Full scale

## Slide 15
Positions of Isometric Axes
Isometric axes can be arbitrarily positioned to create different views of a single object.
Regular
isometric
Reverse axis
isometric
Long axis
isometric
View point is looking
down on the top of
the object.
View point is looking
up on the bottom of
the object.
View point is looking
from the right (or left)
of the object.

## Slide 16
Distance in Isometric Drawing
Isometric line is the line that run parallel to any of the isometric axes.
Isometric axes
True-length distances are shown along isometric lines.
Non-isometric lines

## Slide 18
Isometric
Sketching

## Slide 19
2. Define an isometric axis.
3. Sketching the enclosing box.
4. Estimate the size and relationship of each details.
5. Darken all visible lines.
1. Place the object in the position which its shape and features are clearly seen.
Sketch from an actual object

## Slide 20
STEPS
1. Positioning object.
2. Select isometric axis.
3. Sketch enclosing box.
4. Add details.
5. Darken visible lines.
Sketch from an actual object

## Slide 21
1. Positioning object.
2. Select isometric axis.
3. Sketch enclosing box.
4. Add details.
Note
In isometric sketch/drawing), hidden lines are omitted unless they are absolutely necessary to completely describe the object.
Sketch from an actual object
STEPS
5. Darken visible lines.

## Slide 22
1. Interpret the meaning of lines/areas in multi-view drawing.
2. Locate the lines or surfaces relative to isometric axis.
Sketch from multi-view drawing

## Slide 23
Front View
Top View
Side View
Example 1 : Object has only normal surfaces
Bottom View
Bottom
Front
Side
Side
Front
Top
Regular
Reverse
W
D
H
H
D
W

## Slide 24
Example 2 : Object has inclined surfaces
W
H
q
D
y
x
Front View
y
x
Non-isometric line

## Slide 25
Non-isometric line
A
A
x
y
x
x
B
B
A
B
C
C
C
x
y
Example 3 : Object has inclined surfaces

## Slide 26
A
A
B
B
C
D
E
D
E
F
F
x
y
Front View
Regular
C
Example 4
Reverse

## Slide 27
Circle & Arc in Isometric
In isometric drawing, a circle appears as an ellipse.
2. Construct an isometric square.
3. Sketch arcs that connect the tangent points.
Sketching Steps
1. Locate the center of an ellipse.

## Slide 28
Circle & Arc in Isometric
3. Construct a perpendicular bisector from each tangent point.
4. Locate the four centers.
5. Draw the arcs with these centers and tangent to isometric square.
Sketching Steps
Four-center method is usually used when drawn an isometric ellipse with drawing instrument.
2. Draw a rhombus using diameter of a circle .
1. Locate the center of an ellipse.

## Slide 29
Example 5

## Slide 30
Irregular Curve in Isometric
1. Construct points along the curve in multi-view drawing.
2. Locate these points in the isometric view.
3. Sketch the connecting lines.
Steps

## Slide 34
A
B
C
D
Line
of
sight
Parallel & oblique
to picture plane
Oblique Projection
A
D
C
B

## Slide 35
Oblique Projection
Oblique drawing angle
30o
45o
60o
Type of Oblique drawing
3) General

## Slide 38
Oblique
Sketching

## Slide 39
Object Orientation Guidelines
Place complex features (arc, hole, irregular shape
surface parallel to frontal plane.

## Slide 40
Object Orientation Guidelines
The longest dimension of an object should be
parallel to the frontal plane.
GOOD
WORSE
GOOD
WORSE

## Slide 41
Object Orientation Guidelines
Which orientation is better ?
Not

## Slide 42
D
45
ESTIMATE DEPTH
ESTIMATE LINES
Sketch from actual object

## Slide 43
Sketch from multi-view drawing

## Slide 44
Sketch from multi-view drawing

## Slide 45
A
B
C
D
E
Sketch from multi-view drawing

## Slide 46
A
B
C
D
E
Sketch from multi-view drawing

## Slide 47
A
B
D
E
C
Sketch from multi-view drawing

## Slide 48
A
B
D
E
C
Sketch from multi-view drawing

## Slide 62
THE END!!