## Slide 1: CHAPTER THREE Multi View Drawing

## Slide 2
MULTI-VIEW DRAWINGS
Are convectional projections of a three dimensional object on a two dimensional plane.

## Slide 3
LINE CONVENTION
Precedence of coincide lines.
Hidden line drawing.
Center line drawing.

## Slide 19
VIEW SELECTION STEPS
1. Orient the object to the best position relative to a glass box.
2. Select the front view.
3. Select adjacent views.

## Slide 20
STEP 1 : Orient the Object
The object should be placed in its natural position.
NO !
The object should presents its features in actual size and shape in orthographic views.
GOOD

## Slide 21
STEP 2 : Select a Front View
The object’s longest dimension should be presented as a width.
Inappropriate
First choice
GOOD
Second choice
Waste more space

## Slide 22
Inappropriate
The adjacent views that are projected from the selected front view should appear in its natural position.
STEP 2 : Select a Front View

## Slide 23
STEP 2 : Select a Front View
Choose the view that have the fewest number of hidden lines.
GOOD
Inappropriate

## Slide 24
STEP 3 : Select an Adjacent View
GOOD
Inappropriate
Inappropriate
GOOD
Choose the view that have the fewest number of hidden lines.

## Slide 25
Choose the minimum number of views that can represent the major features of the object.
STEP 3 : Select an Adjacent View
Necessary
Necessary
Hole’s location can be specified on the same view.
Difficult to interprete.
Easy to understand

## Slide 26
Choose the views that are suitable to a drawing space.
STEP 3 : Select an Adjacent View
POOR
Not enough space
for dimensioning.

## Slide 27
Choose the views that are suitable to a drawing space.
STEP 3 : Select an Adjacent View
GOOD

## Slide 28
Example : View selection
Shape description
Size description
F.V.
W
D

W
H

D
mislead to…




F.V. & T.V.
Three views
F.V. & R.S.V.
H

## Slide 29
ONE-VIEW DRAWING
Flat part having a uniform thickness.
Unnecessary
These 2 views provide only information about the part thickness !
1 Thick

## Slide 30
ONE-VIEW DRAWING
Cylindrical-shaped part.
Unnecessary
Repeat !
Infer from CL
Unnecessary

## Slide 31
TWO-VIEW DRAWING
There exists an identical view.
Repeat !
Unnecessary

## Slide 32
The 3rd view has no significant contours of the object.
TWO-VIEW DRAWING
Unnecessary

## Slide 33
TWO-VIEW DRAWING
Unnecessary
The 3rd view has no significant contours of the object.

## Slide 34: Basic Dimensioning

## Slide 35
1. Extension lines
2. Dimension lines
3. Leader lines
4. Dimension numbers
5. Local notes
COMPONENTS
10
27
43
10 Drill, 2 Holes
R16
17

## Slide 50: Drawing layout
All three-dimensional objects have width, height, and depth.
Width is associated with an object’s side-to-side dimension.
Height is the measure of an object from top-to-bottom.
Depth is associated with front-to-back distance.

## Slide 51: Layout of drawing

## Slide 52: Layout of drawing

## Slide 53: Steps to centering the drawing
Step 1; draw border line and title block.

## Slide 54: Step 2; draw diagonal lines from the corners of the net working area.
Diagonal
Point of
intersection

## Slide 55: Step 3; calculate the total horizontal and vertical distance covered by the drawing by considering the space between each view.
Top view
Right side
view
Front view
Width
=
60mm
Space
=20
mm
Depth
=
35
mm
Total horizontal =115mm
Height =45mm
Space =20mm
Depth =
35
mm
Total vertical = 100mm
Hint; take 20mm the space between each view

## Slide 56: Step 4; draw line from the center (point of intersection of the diagonal lines) to half of horizontal and vertical lines
50
mm
50
mm
57.5
mm
57.5
mm

## Slide 57: Step 5; draw the area required for each view.

## Slide 58: Step 6; draw each view.
Construction
line
Note that; except border line, title block and the views all others can be done by using construction line.

## Slide 60
THE END!